## Slide 1: “Seeing” at the Nanoscale: Above the Noise Assignment 2
Andy Ylitalo
November 6, 2019

## Slide 2: Proposed Plan
Analyze X-ray intensity from study of silica dioxide nanoparticles to estimate the lowest concentration at which we can detect a signal (Assignments 1 and 2)
Calculate how the intensity of X-rays changes with the thickness of the tube
Calculate how the intensity of X-rays changes with the size of the nanoparticles

## Slide 3: Key Skills to Learn
How do you quantify “noise”/variation in intensity? (focus of Assignment 2)
How do you isolate the “signal” from the “background?” (completed in Assignment 1)
How you plot the results clearly while changing different variables? (partially covered in Assignment 2)

## Slide 4: Assignment 2
*Learn about “signal-to-noise ratio” @ Khan Academy: https://www.youtube.com/watch?v=MSKYeWfsNO0
Identify peaks
Plot peaks as function of concentration
Plot signal to noise as function of concentration (peak/standard deviation in last column)
Ponder how to estimate the concentration at which we will see 1,2,3 peaks—we should discuss this when you get stuck

## Slide 5: A. Identify 3 Peaks
Star = peak
What is the value of “q” (in 1/A) at which the 50 ppm signal (with background subtracted) reaches each of the three peaks shown above?
*This does not need to be perfect, but try to be within 10% of where you think the true value might be

## Slide 6: B. Plot Peaks as a Function of Concentration
SiO2 concentration (ppm)
Intensity of X-rays
Plateau
Peak 1
Peak 2
Plateau
Peak 1
Peak 2
*Not actual data, just a rough sketch of the next plot to make

## Slide 7: C. Plot Signal to Noise as a Function of Concentration
SiO2 concentration (ppm)
SNR
Plateau
Peak 1
Peak 2
Plateau
Peak 1
Peak 2
*Not actual data, just a rough sketch of the next plot to make
Signal-to-Noise Ratio (SNR): Ratio of the “signal” (in this case, the intensity at one of the three peaks) to the “noise” (we estimate this using the “standard deviation,” the last column of the csv file)

## Slide 8: D. Ponder
How can you determine if a signal is strong enough to be “useful?” (hint: use signal-to-noise ratio)
Based on your proposed definition of a “useful” signal, how high of a concentration is required to see the plateau above the noise? What about peak 1? Peak 2?
*Don’t worry if you can’t figure this out—there’s no perfect answer and I’m happy to discuss